EGRE 365

Lab 4

Driving the seven segment display

Names: ______________________ ______________________ Board # ________

In this lab you will create a project to test the seven-segment display on the Nexys-2 board. The figures below show how the seven-segment display is connected to the FPGA.

Name the project Lab4, and create a Lab4.vhd and a Lab4.ucf file in the project directory. The entity for Lab4.vhd is shown below.

entity Lab4 is

Port ( btns : in std_logic_vector(3 downto 0);

swts : in std_logic_vector(7 downto 0);

leds : out std_logic_vector(7 downto 0);

an   : out std_logic_vector(3 downto 0);

seg  : out std_logic_vector(6 downto 0);

dp   : out std_logic

);

end Lab4;

Develop, synthesize, and demonstrate a Nexys-2 design that satisfies the following specifications,

- The switches control the LED’s. When a switch is up the corresponding LED should be on.

- The switches also control the LED’s of the seven-segment display. When a switch is up the corresponding segment LED should be on.

  - swt(7) turns the decimal point on and off.

  - swt(6) turns segment A on and off.

  - swt(5) turns segment B on and off.

  - etc.

- The buttons controls the particular seven-segment digits. The segments of a seven-segment display must come on only when the corresponding button is pressed. If no buttons are pressed or more than on button is depressed all seven-segment displays are blanked and do not come on.

  - Use a case statement, within a process, to implement this feature.

Signoff: ______________________

After demonstrating the above,  modify your design so that the hex value of the switches is displayed on the seven-segment digits.

- As above at most only one digit, as determined by the buttons, is active at any time.

- The hex value of swts(7 downto 4) are displayed on seven-segment digits 0 and 2.

- The hex value of swts(3 downto 0) are displayed on seven-segment digits 1 and 3.

- The decimal points are not used and should always be off.

Signoff: ______________________