6.7 Exceptions

Explain interrupts using state diagram from chapter 5.

Talk about interrupts on PC.

INT  n

Another source of hazards in a pipeline processor are exceptions or interrupts.

For example, an instruction like add $1, $2, $1 may result in an arithmetic overflow.

When this happens (See section 6.8 for details)

- Instructions must be flushed form the pipeline.

  - To flush IF stage by turning instruction into a NOP.

  - To flush ID stage zero control signals that cause writes.

  - To flush EX stage zero control signals that cause writes.

- Control must be transferred to the exception routine.

  - CU loads PC with address of exception routine.

- The exception routine must be able to return to the point of interruption and resume execution.

  - CU would store return address before transferring control to the exception routine.

  - The exception routine returns by restoring this value to the PC.

Other causes of exceptions

- Processor service request from external device.

- Invoking operating system service by a user program.

- Using an undefined instruction.

- Hardware malfunction.

It can be difficult to associate exception with appropriate instruction.

- 5 instructions are in the pipeline at same time.

  - IF may try to read from a non-existent memory location.

  - ID may encounter an illegal opcode.

  - EX may have an arithmetic overflow.

  - DM may attempt to write to an illegal memory location.

- Multiple exceptions may occur during a given clock cycle.

  - Prioritize interrupts.

    - Interrupt for the earliest instruction is serviced first. Why? Later instructions will be reissued, and can be handled in turn.

- Hardware

  - Stops the exception instruction

  - Let all instructions that came before complete.

  - Flush all that came after.

  - Save the cause of the exception.

  - Save the address of the exception instruction (EPC).

Imprecise interrupts - machine does not always associate the correct exception with the correct instruction.

Most modern machine support precise interrupts.

6.9 Superscalar and Dynamic Pipelining

To achieve faster processors pipelining has been extended:

- Superpipelining - Longer pipelines. Ideally Speedup = k.

  - 8 or more stages.

- Superscalor - Replicate internal components and execute multiple instructions in each stage.

  - Two to six instructions in each stage.

- Dynamic pipeline scheduling or dynamic pipelining.

  - Hardware reschedules instructions to avoid hazards.

  - Example.

lw 	$t0, 20($s2)

addu	$t1, $t0, $t2

sub	$s4, $s4, $t3

slti	$t5, $t4, 20

Note: The lw, addu combination causes a stall, but sub and slti could execute.

We would expect the stall to be for only one clock cycle, but it could be more. We have assumed data is in cache so that it can be accessed in a single clock cycle. But if it is not in cache we must stall for several clock cycles. We will talk about this in the next chapter.

All of above increase complexity.

Superscalar MIPS example. Page 436.

For simplicity:

- Two instructions

- Aligned on 64 bit boundries

- (ALU or Branch) | (Load or store)

See Fig 6.44 p 436

Must add hardware to prevent structural hazards. i.e. GPR must be able to read 4 registers and write 2 registers.

See Figs page 437

Loop Unrolling for superpipelines

Assume loop index is a multiple of 4. See Fig page 440

Dynamic Pipeline Scheduling. See Page 443-445.

Rewritten as:

Loop: lw 	$t0,0($s1)

Addi	$s1,$s1,-4

Addu	$t0,$t0,$s2

Sw	$t0,4($s1)

bne	$s1,$0,Loop

Loop Unrolling assuming index is 4:

Loop:	Addi	$s1,$s1,-16

lw	$t0,16($s1)

lw	$t1,12($s1)

lw	$t2,8($s1)

lw	$t3,4($s1)

addu	$t0,$t0,$s2

addu	$t1,$t1,$s2

addu	$t2,$t2,$s2

addu	$t3,$t2,$s2

sw	$t0,16($s1)

sw	$t1,12($s1)

sw	$t2,8($s1)

sw	$t3,4($s1)

bne	$s1,$0,Loop