Chapter 9 – See book’s CD

Multiprocessors and Clusters

- Building an extremely high performance uniprocessor is very expensive.

- Why not create powerful computers by connecting many microprocessors together?

- Using multiple microprocessors appears to be a cost effective solution.

- Such systems are referred to as:

  - Multiprocessor - parallel processors with a single shared address space.

  - Cluster – A set of microcomputers connected over a local area network.

    - Work well for handling independent tasks.

- Parallel processors may be built using multiple microprocessors or clusters of microcomputers.

How do parallel processors share data?

- Shared memory locations.

  - Used by multiprocessors with a single address space (shared memory processors).

    - All processors are capable of accessing any memory location via loads and stores.

    - Processors can communicate through variables in memory.

    - Synchronization is used to coordinate operations.

    - Two types of shared address space processors.

      - Same amount of time for any processor to access any memory location. Called uniform memory access (UMA) or symmetric multiprocessors (SMP).

      - Some memory accesses are faster than others. Called non-uniform memory access (NUMA).

- Message passing.

  - Used by processors with only private memory. For example clusters of desktop computers.

  - Communicate by sending messages over a local area network.

  - Synchronization is achieved by the sending and receiving of messages.

There are two main methods for connecting multiprocessors.

- Single bus.

- Network.

# Problems with parallel processing

- Limited applications that require many processors.

  - Improvement such as superscalar and out-of-order execution reduces need for multiprocessors.

- Overhead.

- Existing program must be rewritten.

- Programming difficulty.

- Cost – limited number of systems.

- Amdahl’s law.

Recall

Execution time affected by improvement/amount of improvement + Execution time unaffected.

Part of any application is not subject to parallel operations and cannot be improved.

However, this is counteracted by applications changing so that the part that is subject to parallel operations may increase.

See example on pages 9-9, 9-10.

9.3 Multiprocessors connected by a single bus.

Practical with microprocessors.

Parallel Program (Single Bus) Example

Sum 100,000 numbers on a single-bus multiprocessor with 100 processors.

- Distribute the numbers evenly between processors P0 to P99.

- Each processor executes the same program, but with a different Pn. 0 ( Pn ( 99.

sum[Pn] = 0;

for (i = 1000*Pn; i < 1000*(Pn+1); i = i + 1)

sum[Pn] = sum[Pn] + A[i]; /* sum the assigned areas*/

3. Now add the partial sums. Half the processors add pairs of partial sums. Then ¼ of the processors add pairs, etc. till we have the final sum. Note the each processor has its own private “I”.

half = 100; /* 100 processors in multiprocessor*/

repeat

synch(); /* wait for partial sum completion*/

if (half%2 != 0 && Pn == 0)

sum[0] = sum[0] + sum[half-1];

/* Conditional sum needed when half is

odd; Processor0 gets missing element */

half = half/2; /* dividing line on who sums */

if (Pn < half) sum[Pn] = sum[Pn] + sum[Pn+half];

until (half == 1); /* exit with final sum in Sum[0] */

- Cache coherency must be maintained in multiprocessor system.

  - Multiple copies are not a problem when reading.

  - But suppose a processor writes to an address that is in other caches.

- Snooping circuit in each cache controller monitors bus. A write to shared data must either invalidate or update that data in all cache memories.

- Duplicate tag bits are used for snooping so that the snooping does not interfere with the processor.

- Write back and write invalidate is used to reduce bus traffic.

Inter processor communication is achieved by passing message between processors on the network.

Parallel Program (Message Passing) Example

Sum 100,000 numbers on a network connected multiprocessor with 100 processors.

- Since this compute has multiple address spaces, distribute the 100 subsets to the processors local memories.

- Let each processor sum its subset.

sum = 0;

for (i = 0; i<1000; i = i + 1) /* loop over each array */

sum = sum + A1[i]; /* sum the local arrays */

3. Each partial sum is in a different execution unit (processor); therefore, we must use network message passing to send and receive partial sums.

limit = 100; half = 100;/* 100 processors */

repeat

half = (half+1)/2; /* send vs. receive dividing line*/

if (Pn >= half && Pn < limit) send(Pn - half, sum);

if (Pn < (limit/2)) sum = sum + receive();

limit = half; /* upper limit of senders */

until (half == 1); /* exit with final sum */

Example using six processors to sum 6 X 3 items, a(0)-a(17).

Addressing in Large-Scale Processors

- Most commercial large-scale processors use memory that is distributed.

  - Very difficult and expensive to build a shared memory machine that can scale up to scores of processors and scores of memory modules.

- Send and Receive is used for communication.

  - A shared memory machine can use load and stores for communication.

Network Topologies.

Ring –

#Links = N

Max Distance (diameter) D = N/2

Degree = 2

Bisection BW = 2

#Links = 2N2

D =      BBW = 2n

Degree = 4

#Links =

D = 1, Degree = N-1, BBW = (P/2)2

Hypercube

| N | n = Log2N | # Links assume N power of 2 | Distance |  |
| --- | --- | --- | --- | --- |
| 1 | 0 | 0 | 0 |  |
| 2 | 1 | 1 | 1 |  |
| 4 | 2 | 1*2+2 = 4 | 2 |  |
| 8 | 3 | 4*2+4 = 8/2 * 3 = 12 | 3 |  |
| 16 | 4 | 12*2 + 8 = 3*8 + 8 = 16/2 * 4 | 4 |  |
| N | Log2N | N/2 * Log2N | Log2N |  |

# Text boxes

Barrier synchronization (wait for all processors)