EGRE 426

Homework # 1

Due Monday 9/1/09

Solutions

Assume each operation take one unit of time and zero delay for communication or memory access so that all data is available when needed.

- (a). For a single processor SISD machine show the fastest way to compute when n = 6.

(b). Write a general expression for T(n) that is valid for any n > 0.

Solution:

| Time |  |
| --- | --- |
| 1 | x |
| 2 | x |
| 3 | + |
| 4 | x |
| 5 | + |
| 6 | x |
| 7 | + |
| 8 | x |
| 9 | + |
| 10 | x |
| 11 | + |

T(6) = 11. In general, since the SISD can do only one operation at a time T(n) = total number of operations = number of adds + number of multiplications = (n-1) + n = 2n-1

- (a). Repeat 1(a) and (b) for a SIMD computer with unlimited processors.

(b). Obtain the speedup, as a function of n, of the SIMD compared with the SISD.

(c). What is the order of the speedup?

(d). Assume n is a power of two and that only  p = n processors are used , what is the efficiency E as a function of n?

(e). What is the order of the efficiency?

Solution:

| Time |  |
| --- | --- |
| 1 | x x x x x x |
| 2 | + + + |
| 3 | + |
| 4 | + |

T(6) = 4. In general, T(n) = time to perform n multiplications simultaneously + time to fan in the addition of the n product terms = .

, since

- (a). Using an unlimited number of processors show the fastest way to compute  for n = 6 on a MIMD machine.

(b). What is the fewest number of processors that could be used to compute F in the shortest possible time?

(c). Show how this can be done.

(d). What is the efficiency in (c).

Solution:

| Time |  |
| --- | --- |
| 1 | x x x x x x |
| 2 | + + + |
| 3 | + |
| 4 | + |

T(6) = 4. In general the solution is the same for the SIMD machine.

However, on the MIMD machine the same computation could be done, in the same time, using only 4 processors.

| Time |  |
| --- | --- |
| 1 | x x x x |
| 2 | + + x x |
| 3 | + + |
| 4 | + |

Consider the computation of

4. For a SISD machine, what is the fastest time in which F can be computed for n = 4?

ANS: T(4) = 7

5. Write the expression for the fastest time for any value of n?

ANS:

6.  For a SIMD machine with unlimited processors, what is the fastest time in which F can be computed if n = 4?

ANS: T(4) = 2 + 2 + 1 = 5.

7. Write the expression for the fastest time for any value of n?

ANS:

8. For a MIMD machine with unlimited processors, what is the fastest time in which F can be computed if n = 4?

ANS:  T(4) = 2 + 1 = 3

9. Write the expression for the fastest time for any value of n?

ANS:

10. When n = 4 what is the speedup achieved using the MIMD machine in problem 10 compared to the SISD machine in problem 6.

ANS: