EGRE 426

Homework

Due 9/17/07

Work the following problem in the textbook.

2.4

2.6  Using MIPS instructions perform the operation:

$t0 ( 015||$t3(22..6)

2.13 Use the C code given in 2.13 and write MIPS assembly language to perform the same function. Let i be in $a0, x be in $a1, and y in $a2. The control flow graph is shown below.

2.29 Let $a0 = a, $a1 = b

2.30

2.31

2.32 Show the minimal sequence of MIPS instructions for the C statement.

b = 25 | a;

8. SPIM problem.

Download the file count1s.asm form the class web page and complete the subroutines jcnt and count1s. Run count1s.asm on the spim simulator. The correct output is shown below. Be sure the Spim Simulator ( settings are as shown. Delayed Branches must be turned off.

main:

sw      $ra,0($sp)  #Push return address

addiu   $sp,$sp,-4  # onto stack

#

la      $a0,start   #Point to start message

jal     wr_str      #Output start message

# Start counting

and     $a0,$0,$0   #Clear $a0

loop:

jal     wr_hex      #Output count in hex

jal     space       #Output a space

and     $t0,$a0,$a0 #Save $a0

jal     count1s     #Put number of 1's in $a1

and     $a0,$a1,$a1 #Move count to $a0

jal     wr_int      #Output count

jal     crlf        #Go to new line

and     $a0,$t0,$t0 #Restore $a0

jal     jcnt        #Johnson count inc $a0

bne     $a0,$0,loop #Loop till $a0 is 0

#

exit:   la      $a0,done    #Use pseudoinstruction

jal     wr_str      #Output done message

#

addiu   $sp,$sp,4   #Pop return address

lw      $ra,0($sp)  # from stack

jr      $ra         #Return

###################################################

# FUNCTION: jcnt - Implements a Johnson counter. When called

#           the count in $a0 to the next value as shown below.

#                ...

#             00000000H

#             80000000H

#             C0000000H

#             E0000000H

#             F0000000H

#             F8000000H

#                ...

#             FFFFFFFFH

#             7FFFFFFFH

#                ...

#             00000003H

#             00000001H

#             00000000H

#             80000000H

#                ...

#   INPUTS: $a0 -

#  OUTPUTS: $a0 -

# DESTROYS: $a0, $t0

###################################################### Do not use pseudoinstructions, and do not assume particular

# values in any register. Change only $a0 and $t0.

# Comment your code!

jcnt:

# Enter your code here.

jr      $ra             #Return

###################################################### FUNCTION: count1s - Returns in $a1 the count of the number

#           of 1's in $a0

#    INPUT: $a0 - Input register

#   OUTPUT: $a1 - Output of 1's in $a0

#    CALLS: NONE

# DESTROYS: $a0,$a1

###################################################### Do not use pseudoinstructions, and do not assume

# values in any register. Change only $a0 and $a1.

# Comment your code!

count1s:

# Enter your code here.

jr      $ra