EGRE 426

Homework _ Solutions

Due 9/15/09

Work the following problem in the textbook.

2.4 A subtract immediate instruction is not necessary since the addi can be used for this function by making the offset negative.

2.6 Using MIPS instructions perform the operation:

$t0 ( 015||$t3(22..6)

One possible solution is shown below. Why doesn’t it work?

wrong:

andi	$t0, $t3, 0000_0000_0111_1111_1111_1111_11XX_XXXX

# Keep field

srl	$t0, $t3, 6	# Move field into rightmost bits

Can you find the two errors?

The immediate value must be only 16 bits. The second instruction should be srl $t0,$t0,6

A correct solution is:

right:

sll	$t0,$t3,9       #Shift t3 left 9 places and store in t0

srl	$t0,$t0,15     #Move field to least significant end

I simulated this program using PCSPIM the actual program is shown below:

# Test for problem 2.6

.text         #Code goes in text segment

.globl  main

#############################################

main:

sw      $ra,0($sp)  #Push return address

addiu   $sp,$sp,-4  # onto stack

#

lui     $t3,0xFFD5  #Put FFD5A5AFH

ori     $t3,0xA5AF  # in $t3

jal     P2_6     #Call subroutine of problem 3.6

#

addiu   $sp,$sp,4   #Pop return address

lw      $ra,0($sp)  # from stack

jr      $ra         #Return

###############################################

# FUNCTION: P2_6 $t3 <-- 0..0||$t3(22..6)

#           For example if $t0 = FFD5A5AH before call

#           $t3 = 00015696 on return from P2_6.

#   INPUTS: $t3 - Contains field in bits 22..6

#  OUTPUTS: $t0 - field in LS bits 0 elsewhere.

# DESTROYS: $t0

###############################################

P2_6:

sll     $t0,$t3,9    #Clear MS bits

srl     $t0,$t0,15   #Move fiels to LS bits

jr      $ra          #Return

2.13 And write MIPS assembly language to perform the same function. Let i be in $a0, x be in $a1, and y in $a2.

add	$a0,$0,$0		# Set i to 0

loop:		beq	$a0,$a1,exit		# Exit when i = x. Assumes x positive

add	$a2,$a2,$a0		# y = y + i

addi	$a0,$a0,1		# i = i + 1

j	loop

2.29 $a0 = a, $a1 = b

add	$t0, $0, $0		# Clear $t0

loop:		beq	$a1, $0, finish	# Jump to finish if  $a1 = 0

add	$t0, $t0, $a0		# Put running sum in $t0

addi	$a1, $a1, -1		# Do loop $a1 times

j	loop

finish:		addi	$t0, $t0, $100	# add 100 to a * b

add	$v0, $t0, $0		# move $t0 to $v0

Program computes a*b + 100 or  $v0 ( $a0 * $a1 + 100

My rewrite (unverified) without using the mul instruction.

addi	$v0, $0, 100		# put 100 in $v0

loop:		beq	$a1, $0, finish	#done if $a1 = 0

add	$v0, $v0, $a0	# compute 100 + $a0*$a1

addi	$a1, $a1, -1		# decrement $a1

j	loop

finish:

2.30

The code determines the number of matching elements between the two arrays and returns this number in register $v0.

2.32 Show the minimal sequence of MIPS instructions for the C statement.

b = 25 | a;

ori	$b, $a, 25

Here I am using $a and $b for the MIPS register that contains a and b respectively.

8. SPIM problem.

Download the file count1s.asm form the class web page and complete the subroutines jcnt and count1s. Run count1s.asm on the spim simulator. The correct output is shown below. Be sure the Spim Simulator ( settings are as shown. Delayed Branches must be turned off.

main:

sw      $ra,0($sp)  #Push return address

addiu   $sp,$sp,-4  # onto stack

#

la      $a0,start   #Point to start message

jal     wr_str      #Output start message

# Start counting

and     $a0,$0,$0   #Clear $a0

loop:

jal     wr_hex      #Output count in hex

jal     space       #Output a space

and     $t0,$a0,$a0 #Save $a0

jal     count1s     #Put number of 1's in $a1

and     $a0,$a1,$a1 #Move count to $a0

jal     wr_int      #Output count

jal     crlf        #Go to new line

and     $a0,$t0,$t0 #Restore $a0

jal     jcnt        #Johnson count inc $a0

bne     $a0,$0,loop #Loop till $a0 is 0

#

exit:   la      $a0,done    #Use pseudoinstruction

jal     wr_str      #Output done message

#

addiu   $sp,$sp,4   #Pop return address

lw      $ra,0($sp)  # from stack

jr      $ra         #Return

###################################################

# FUNCTION: jcnt - Implements a Johnson counter. When called

#           the count in $a0 to the next value as shown below.

#                ...

#             00000000H

#             80000000H

#             C0000000H

#             E0000000H

#             F0000000H

#             F8000000H

#                ...

#             FFFFFFFFH

#             7FFFFFFFH

#                ...

#             00000003H

#             00000001H

#             00000000H

#             80000000H

#                ...

#   INPUTS: $a0 -

#  OUTPUTS: $a0 -

# DESTROYS: $a0, $t0

###################################################### Do not use pseudoinstructions, and do not assume particular

# values in any register. Change only $a0 and $t0.

# Comment your code!

jcnt:

# Enter your code here.

jr      $ra             #Return

###################################################### FUNCTION: count1s - Returns in $a1 the count of the number

#           of 1's in $a0

#    INPUT: $a0 - Input register

#   OUTPUT: $a1 - Output of 1's in $a0

#    CALLS: NONE

# DESTROYS: $a0,$a1

###################################################### Do not use pseudoinstructions, and do not assume

# values in any register. Change only $a0 and $a1.

# Comment your code!

count1s:

# Enter your code here.

jr      $ra

Solution:

jcnt:

xori    $a0,$a0,1       #Complement LSB of $a0

srl     $t0,$a0,1       #Do rotate by shifting

sll     $a0,$a0,31	  #and oring in

or      $a0,$a0,$t0	  #least significant bit

jr      $ra             #Return

###############################################################

# FUNCTION: count1s - Returns in $a1 the count of the number

#           of 1's in $a0

#    INPUT: $a0 - Input register

#   OUTPUT: $a1 - Output of 1's in $a0

#    CALLS: NONE

# DESTROYS: $a0,$a1

###############################################################

# Do not use pseudoinstructions, and do not assume particular

# values in any register. Change only $a0 and $a1.

# Comment your code!

count1s:

and     $a1,$0,$0       #Clear count

cloop:

bgez    $a0,zero        #Check most sig bit of $a0

addi    $a1,$a1,1       #If it is 1, Increment count

zero:

sll     $a0,$a0,1       #Move next bit to most sig position

bne     $a0,$0,cloop    #Loop till no more 1's

jr      $ra