# Mips Instruction Set

# Version 5.1

# MIPS Programmer Accessible Registers and Memory

The MIPS contains the following:

A program counter register that contains the address of the instruction to be executed.

# PC = PC(31..0)

32 general purpose 32 bit registers.

# GPR = GPR(0..31) = GPR(0..31; 31..0)

A byte addressable memory with 32 bits of address.

# MB = MB(0..0FFFFFFFFH) = MB(0..0FFFFFFFFH; 7..0)

Certain special purpose registers including:

# LO = LO(31..0), HI = HI(31..0)

For convenience we will define the following registers and memory in terms of the above.

# Ri = GPR(i), Note: R0 ( 0

Note: In place of Ri the MIPS assembler uses $i.

Thus, to add the contents of R8 to R9 and put the result in R10 the assembly language instruction is: add $10,$8,$9

# MH(n0) = MH(n0; 15..0) = MB(n0)||MB(n0+1)

where 0 (  n0 ( 0FFFFFFFEH and n0 is even.

# M(n00) = M(n00; 31..0) = MB(n00)||MB(n00+1)||MB(n00+2)||MB(n00+3)

where 0 ( n00 ( 0FFFFFFFCH and n00 is a multiple of 4

(i.e. n00 addresses a word boundary).

A detailed description of the assembly language instructions can be found in the MIPS R4000 Microprocessor User’s Manual available at http://www.mips.com/publications/index.html.

MIPS instruction format

I - Type instruction

| 31 6 | 5 | 5 | 16 0 |
| --- | --- | --- | --- |
| Opcode | rs | rt | n/offset |

R - Type

| 6 | 5 | 5 | 5 | 5 | 6 |
| --- | --- | --- | --- | --- | --- |
| Opcode | rs | rt | rd | shamt | func |

J - Type

| 6 | 26 |
| --- | --- |
| Opcode | raddr |

Definitions: 016 ( n ( 116, 016 ( ofst ( 116, 05 ( sa ( 15, 026 ( addr ( 126

rd, rs, rt ( ($0,…,$31)

| Notation | Interpretation | Example |
| --- | --- | --- |
| 1k | k bits of 1 | 13 = 111 |
| 0k | k bits of 0 | 04 = 0000 |
| n(k) | The k th bit of n | if n = 1000H then n(12) = 1 |
| ¦¦ | concatenation | 02¦¦13¦¦04 = 001110000 |
| (n | n(15)16¦¦n i.e. n sign extended to 32 bits. | (7654H = 00007654H, (8654H = FFFF8654H |

Notes: Unless specified differently PC ( PC+4 for each instruction. $0 ( 0 even if written to. To be compatible with SPIM we assume branches are not delayed.

|  |  | Arithmetic and Logical Instructions. | Exceptions |
| --- | --- | --- | --- |
| add | rd,rs,rt | rd ( rs + rt | If iov rd ( rd |
| addi | rt,rs,n | rt ( rs + (n | If iov rt ( rt |
| addiu | rt,rs,n | rt ( rs + (n | none |
| addu | rd,rs,rt | rd ( rs + rt | none |
| and | rd,rs,rt | rd ( rs & rt | none |
| andi | rt,rs,n | rt ( rs & 016¦¦n | none |
| div | rs,rt | LO ( Int(rs/rt), HI ( rs % rt | none |
| divu | rs,rt | LO ( Int(rs/rt), HI ( rs % rt | none |
| mult | rs,rt | HI¦¦LO ( rs x rt | none |
| multu | rs,rt | HI¦¦LO ( rs x rt | none |
| nor | rd,rs,rt | rd ( ~(rs ¦ rt) | none |
| or | rd,rs,rt | rd ( rs ¦ rt | none |
| ori | rt,rs,n | rt ( rs ¦ 016¦¦n | none |
| sll | rd,rt,sa | rd ( rt(31-sa..0)¦0sa or rd ( rt << sa | none |
| sllv | rd,rt,rs | same as sll with sa = rs(4..0) | none |
| sra | rd,rt,sa | rd ( rt(31)sa¦¦rt(31..31-sa) | none |
| srav | rd,rt,rs | same as sra with sa = rs(4..0) | none |
| srl | rd,rt,sa | rd ( 0sa¦¦rt(31..31-sa) | none |
| srlv | rd,rt,rs | same as srl with sa = rs(4..0) | none |
| sub | rd,rs,rt | rd ( rs - rt | If iov rd ( rd |
| subu | rd,rs,rt | rd ( rs – rt | none |
| xor | rd,rs,rt | rd ( rs ^ rt or rd ( rs ( rt | none |
| xori | rt,rs,n | rt ( rs ^ 016¦¦n or rt ( rs ( 016¦¦n | none |

# Constant-Manipulating Instructions

|  |  | Constant-Manipulating Instructions | Exceptions |
| --- | --- | --- | --- |
| lui | rt,n | rt ( n¦¦016 | none |
|  |  | Comparison Instructions |  |
| slt | rd,rs,rt | If rs < rt then rd ( 1 else rd ( 0 | none |
| sltu | rd,rs,rt | If rs < rt then rd ( 1 else rd ( 0 | none |
| slti | rt,rs,n | if rs < (n then rt ( 1 else rt ( 0 | none |
| sltiu | rt,rs,n | if rs < (n then rt ( 1 else rt ( 0 | none |
|  |  | Branch Instructions |  |
| beq | rs,rt,ofst | if rs = rt then PC ( PC + 4 + (ofst¦¦00 else PC ( PC+4 | none |
| bgez | rs,ofst | if rs(31) = 0 then PC ( PC + 4 + (ofst¦¦00 else PC ( PC+4 | none |
| bgezal | rs,ofst | $31 ( PC?, if rs > 0 then PC ( PC + 4 + (ofst¦¦00 else PC ( PC+4 | none |
| bgtz | rs,ofst | if rs(31) = 0 and rs ( 032 then then PC ( PC + 4 (ofst¦¦00 else PC ( PC+4 | none |
| blez | rs,ofst | if rs ( 0 then then PC ( PC + 4 + (ofst¦¦00 else PC ( PC+4 | none |
| bltzal | rs,ofst | $31 ( PC, if rs ( 0 then then PC ( PC + 4 + (ofst¦¦00 else PC ( PC+4 | none |
| bltz | rs,ofst | if rs < 0 then then PC ( PC + 4 + (ofst¦¦00 else PC ( PC+4 | none |
| bne | rs,rt,ofst | if rs ( rt then then PC ( PC + 4 + (ofst¦¦00 else PC ( PC+4 | none |
|  |  | Jump Instructions |  |
| j | addr | PC ( PC(31..28)¦¦addr¦¦00 | none |
| jal | addr | $31 ( PC+4, PC ( PC(31..28)¦¦addr¦¦00 | none |
| jalr | rs | $31 ( PC+4, PC ( rs | none |
| jalr | rd,rs | rd ( PC+4, PC ( rs | none |
| jr | rs | PC ( rs |  |

|  |  | Load and Store Instructions |  |
| --- | --- | --- | --- |
| lbu | rt,ofst(rs) | rt ( 024¦¦MB(rs + (ofst) or rt ( MB(rs + (ofst) | yes |
| lb | rt,ofst(rs) | rt ( MB(rs + (ofst;7)24¦¦MB(rs + (ofst) or rt ( (MB(rs + (ofst) | yes |
| lhu | rt,ofst(rs) | rt ( MH(rs + (ofst) | yes |
| lh | rt,ofst(rs) | rt ( (MH(rs + (ofst) | yes |
| lw | rt,ofst(rs) | rt ( M(rs + (ofst) | yes |
| lwl | rt,ofst(rs) | let va = rs + (offst and assume Big-endian if va(1,0) = 00 then rt ( M(va) if va(1,0) = 01 then rt ( MB(va)¦¦MB(va+1)¦¦MB(va+2)¦¦rt(7..0) if va(1,0) = 10 then rt ( MB(va)¦¦ MB(va+1)¦¦rt(15..0) if va(1,0) = 11 then rt ( MB(va)¦¦ rt(23..0) | yes |
| lwr | rt,ofst(rs) | let va = rs + (offst if va(1,0) = 00 then rt ( rt(31..8)¦¦MB(va) if va(1,0) = 01 then rt ( rt(31..16)¦¦MB(va)¦¦MB(va+1) if va(1,0) = 10 then rt ( rt(31..24)¦¦MB(va)¦¦ MB(va+1)¦¦MB(va+2) if va(1,0) then rt ( M(va-3) | yes |
| sb | rt,ofst(rs) | MB(rs + (ofst) ( rt(7..0) | yes |
| sh | rt,ofst(rs) | MH(rs + (ofst) ( rt(15..0) | yes |
| sw | rt,ofst(rs) | M(rs + (ofst) ( rt | yes |
| swl | rt,ofst(rs) | let va = rs + (offst and assume Big-endian if va(1,0) = 00 then M(va) ( rt if va(1,0) = 01 then MB(va)¦¦MB(va+1)¦¦MB(va+2) ( rt(31..24) if va(1,0) = 10 then MB(va)¦¦ MB(va+1)¦¦rt(15..0) ( rt(31..16) if va(1,0) = 11 then MB(va) ( rt(31..24) | yes |
| swr | rt,ofst(rs) | let va = rs + (offst if va(1,0) = 00 then rt ( rt(31..8)¦¦MB(va) if va(1,0) = 01 then rt ( rt(31..16)¦¦MB(va)¦¦MB(va+1) if va(1,0) = 10 then rt ( rt(31..24)¦¦MB(va)¦¦ MB(va+1)¦¦MB(va+2) if va(1,0) then rt ( M(va-3) | yes |
| mfhi | rd | rd ( hi |  |
| mflo | rd | rd ( lo |  |
| mthi | rs | hi ( rs |  |
| mtlo | rs | lo ( rs |  |

# Footnotes

H is for hexadecimal, B for binary.

These 5 bits specify which register is rs.

Integer overflow

rs and rt are treated as 2’s complement integers. The quotient is placed in LO and the remainder in HI.

rs and rt are treated as unsigned integers. The quotient is placed in LO and the remainder in HI.

rs and rt are treated as 2’s complement integers.

rs and rt are treated as unsigned integers.

rs and rt are treated as signed integers.

rs and rt are treated as unsigned integers.

rs and (n are treated as signed integers.

rs and (n are treated as unsigned integers.