## Slide 1: Skeletal Imaging
IN NUCLEAR MEDICINE

## Slide 2: Required Reading
SNMMI Procedures Standard for Bone Scintigraphy 4.0
  https://www.snmmi.org/ClinicalPractice/content.aspx?ItemNumber=6414#Skeletal
Information in the presentation follows the procedures standards set forth by SNMMI on bone scintigraphy
  Please refer to these standards for further clarification on bone imaging procedures
Additional information can be found on numerous other procedures standards by SNMMI
  https://www.snmmi.org/ClinicalPractice/content.aspx?ItemNumber=6414

## Slide 3: PART I
In this section we will discuss
Anatomy and Physiology of the Skeletal system
MDP and the mechanism of uptake
Compounding MDP

## Slide 4: Clinical Indications and Applications
Detect skeletal lesions at earliest possible time
Staging of skeletal disease
Evaluate metabolic activity of skeletal disease
Commonly used to image metastases (mets)
  Primary cancer that has spread to another site

## Slide 5: Studies
Bone Imaging
Whole Body Bone Imaging
Three-Phase Bone Imaging
  For the assessment of osteomyelitis

## Slide 6: Why Utilize a Bone Scan?
High sensitivity compared to other modalities
  Ability to detect when something is wrong
  30-50% of the bone must be decalcified before tumors or infection can be detected with x-rays
  Bone Scan only requires 1 – 2% (~15%) decalcification to yield abnormal bone scan
Issue – there is low specificity
  Ability to identify a specific disease state
  Example is it a fracture or is it metastatic disease?

## Slide 7: A little History of the Radiopharmaceuticals
First attempts – 32P and 45Ca (Pure Beta)
Then came the mix emitters – 47Ca and 85Sr and 87mSr
  Energies where 1.3 meV, 513 keV and 388 keV
  T1/2 65 days to 2.9 days
Revolution in imaging and radiopharmaceuticals
  99mTcPYP/PYR
  Diphosphonates – 99mTcMDP/HDP
Resurgence of Na18F (PET)
7

## Slide 8: Primary Radiopharmaceutical Used in Bone Imaging
99mTc MDP
Medronate (brand)
Methylene diphosphantic acid (generic)

## Slide 9: What is the composition of Bone Tissue?
Approximately 30% organic and 70% inorganic
  90 to 95% of organic bone is made up of collagen and mucopolysaccharides
  Majority of bone is inorganic. This crystalline structure is also referred to as : boney matrix or the hydroxyapatite
    It is composed of calcium, phosphorus (mostly found as phosphate)
    To a lesser amount – sodium, magnesium, potassium, chloride, and fluorine
Bone tissue is similar to and associated with connective tissue
While bone consists of living tissue the predominant amount is non-living bone has been calcified.

## Slide 10: Factors that Affect Bone Development
Nutritional needs include calcium, protein, magnesium, phosphorus, vitamin D, Fluoride, potassium
Exposure to sunlight creates Vitamin D for bone development
Physical exercise causes bone tissue to develop and become denser/stonger
Hormonal secretions – refer to the next slide

## Slide 11: Hormonal secretions and Bone Growth
Stimulate activity in the epiphyseal (growth) plates via
  Growth Hormone-1 stimulate formation/absorption
  Parathyroid hormone to regulate calcium levels and growth
  Estrogen and testosterone assist in strengthening bone
Pediatrics bone development
  Cartilage/soft bone undergo primary ossification at the epiphyseal plate
  The diaphysis is “left behind” where osteoblastic cells ossify the organic tissue

## Slide 12: Bone Lesions have Increase or Decreased Activity
Increased concentration of radiopharmaceutical is commonly osteoblastic activity (this is more common)
Decreased concentration of radiopharmaceutical is commonly osteoclastic activity (e.g. lytic lesion)
https://www.sciencephoto.com/media/934626/view/metastatic-renal-cell-carcinoma-bone-scan
https://www.researchgate.net/publication/273278778_Prolonged_survival_in_a_patient_with_isolated_skull_recurrence_of_cervical_carcinoma_-_Case_report_and_review_of_the_literature/figures?lo=1

## Slide 13: Hydroxyapatite Crystal
Inorganic constituent of bone matrix and teeth
Forms lattice structure composed of calcium, phosphate and hydroxyl ions
    Strength and density

## Slide 14
Continuous interchange of ions between crystal lattice and the fluid that bathes it
RP localizes in the hydroxyapatite (HA) crystal via adsorption and ion exchange (chemisorption)
  Specifically any phosphate exchanges with calcium on the HA cystal
    99mTcMDP, 99mTcHDP, 99mTcPYP,

## Slide 15: Radiopharmaceutical - Mechanism of Localization
Chemisorption
Bone tissue is comprised of organic and inorganic substances. The inorganic portion (bone matrix) consists of hydroxyapatite crystals that are composed of calcium, phosphate, and other mineral components
Localization of the imaging agent is through the exchange of ions native to the bone tissue with ions from our labeled radiopharmaceutical

## Slide 16: Mechanism of Localization
Calcium phosphate is a main component of bone tissue
When a bone is injured or affected by a disease process, calcium phosphate will go to the site to repair and build new bone
Radiolabeled phosphate compounds will undergo ion exchange at these sites through chemisorption
Two major factors control accumulation of phosphates in bone
  1) Blood flow - skeletal vascularity
  2) Extraction efficiency
  Rate of new bone formation (Osteoblastic activity)
↓ Decreased uptake will occur in
  Impaired or no blood flow (bone infarct)
  Complete destruction (AVN- avascular necrosis)
  Abscesses
  Replacement by benign tumor

## Slide 17: Other areas of Radiopharmaceutical Accumulation
Factors that effect MDP uptake
  Soft tissue uptake
  Renal impairment
  Decreased cardiac output
  Dehydration
  Extravasation of the radiopharmaceutical
  Aging
  Under dosage of radiopharmaceutical
  Obesity

## Slide 18: Normal Skeletal Uptake
Uptake of the radiopharmaceutical is symmetrical
Normal uptake
  Sacroiliac joints
  Hip joints
  Glenoid fossa
  Acromioclavicular joints
  Sternoclavicular joints
  Ends of long bones
  Growing epiphyses - pediactric
  Vertebral column

## Slide 19: MDP Kit Contains
Medronic Acid (ligand)
Stannous Chloride Dihydrate or Stannous Fluoride (reduces valence from +7 to +4)
Antioxidant, such as ascorbic acid (depends on manufacturer)
  Introduction of oxygen into the kit will reduce the tagging by increasing the amount of free tech
ALL RPs have sodium hydroxide and/or hydrochloric acid in them for pH adjustment

## Slide 20: MDP Kit Preparation
Add the pertechnetate
  The maximum activity is set by the manufacturer
  DraxImage has a max of 500 mCi in 2 mL to 10 mL
  Saline may be added when compounding
    Do not inject air into the vial – this may break down the tagged compound
Mix for 1-2 minutes by swirling the vial
Store at 20-25 ºC before and after compounding
Expires in 6 hours
For more information on compounding see package insert - https://www.accessdata.fda.gov/drugsatfda_docs/label/2011/018035s032lbl.pdf

## Slide 21: Part II
Bone Procedures
Administration and Patient Preparation
Patient Positioning
Three Phase Bone Scan
Limited Bone Scan
Pinhole Imaging
SPECT Bone
Other Spot views
May perform all four on the same patient

## Slide 22: Administration
10-30 mCi (370 MBq – 1.11 GBq) dose for both MDP
  Unless otherwise indicated this is the standard dose range for all bone imaging procedures
Method of Administration - IV bolus
For three-phase bone scan, injection must occur while on gamma camera to visualize blood flow of radiopharmaceutical
  Immediately when injecting dynamic blood flow
  Immediately following phase 1, static blood pool
  Delay 3 hour skeletal imaging

## Slide 23: Post Administration
Begin imaging 2-3 hours post injection
  In normal radiotracer distribution approximately three hours after injection you will have 50% of the activity seen in the skeleton
  The other 50% will be excreted through the kidneys

## Slide 24: Patient Preparation
Patient may eat or drink as normal
After administration of radiopharmaceutical, the patient must wait 2-3 hours before imaging
  This is to allow the radiopharmaceutical to collect in the bone and to reduce the amount of background activity in the soft tissue which is eliminated through the kidneys

## Slide 25: Patient Preparation
Instruct the patient to drink 6-8 glasses of a liquid (1 liter or more). This will help to concentrate the radiopharmaceutical into the bone and not the soft tissue
Soft tissue uptake can increase with poor renal function or dehydration
To reduce the radiation burden to the bladder tell the patient to urinate often
Just prior to image acquisition have the patient void – A radioactive urinary bladder can mask bone lesion in that vicinity

## Slide 26: Contraindications
Recent Tc99m study (24-48 hours)
Barium contrast may cause attenuation
Colloidal formation from the drug interaction
Barium Contrast

## Slide 27: Normal Skeletal Uptake
Uptake of the radiopharmaceutical is symmetrical
Normal uptake
  Sacroiliac joints
  Hip joints
  Glenoid fossa
  Acromioclavicular joints
  Sternoclavicular joints
  Ends of long bones
  Growing epiphyses - pediactric
  Vertebral column

## Slide 28: Patient Positioning
Clothes are no problem
Void and remove attenuators
Prostate CA
  Patient that cannot eliminate most of their urine may require catheterization. Concern – masking mets in the pelvic

## Slide 29
Make the patient comfortable.
  Pillow for head support
  Pillow under knees – improves lumbar curvature
Patient must hold still
Foot band to line up joints for A/P acquisition
Patient Positioning
https://pillowreviewer.com/
https://www.flickr.com/

## Slide 30: Three Phase Bone Scan
Bone scan with flow, capable of detecting:
  Infection
  Stress fracture (fx)
  Avascular necrosis (AVN)
  Vascularity of lesion
  Osteomyelitis
  Cellulitis

## Slide 31: Phase 1 – Blood flow
Include both ROI and contra-lateral in FOV
Bolus injection
At a 64 x 64 or 128 by 128 matrix immediately record dynamic flow images every 2-4 seconds for 60 seconds
Vascular flow to area

## Slide 32: Phase II – Tissue/Blood pooling
Blood pools or immediate statics
  Same position as flow
  To be performed immediately following the flow
  500k count statics or 3-5 minutes (256 x 256 matrix)
Soft tissue phase - Perfusion in area
Sometimes referred to as
“immediate” images
Complete within 10 minutes post injection

## Slide 33: Phase III – Delay/Bone activity
Routine bone scan – patient returns 2-3 hours post dose – Spots views are usually taken, but whole body may be considered
Spot view
  Matrix size 256 x 256
  Low Energy Parallel Whole collimator
  Acquisition 3-500k or 5 minute is
  acceptable for the appendages
Delay phase - Bone metabolism
  Follow the same setting for spot view
SNMMI Procedure Standard for Bone Scintigraphy 4.0
- Refer to procedures guideline for more detail

## Slide 34: Cellulitis
Activity shows increased uptake on flow (A) and immediate static (B), but there is “normal“ issue uptake in the delays ©
https://www.researchgate.net/figure/Example-images-of-cellulitis-arrows-Significant-uptake-of-99m-Tc-MDP-is-seen-in-left_fig2_51526933
Hyperaemia (also hyperemia) - is the increase of blood flow to different tissues in the body. It can have medical implications but is also a regulatory response, allowing change in blood supply to different tissues through vasodilation.

## Slide 35: Phase Four
On a rare occasion a fourth phase maybe required
This occurs when there is excessive background activity
Images may be requested for up to 24 hours post inject
Cause
  Renal insufficiency
  Diabetic
  Cellulitis vs Osteomyelitis (image D is 24 hours)
Spot imaging only of ROI at 24 hours
  Do to the lack of activity imaging acquisition may set for 20 minutes instead of counts

## Slide 36: Whole Body Bone Scan (WBB)
Most common skeletal procedure
Inject IV
Scan 2-4 hours post injection
Camera
  256 x 1024 Matrix
  Low Energy Parallel Whole (LEPH)
  Scan speed 16 cm or less
Supine on table
Knee pillow
Binder or band around feet/toes
SNMMI Procedure Standard for Bone Scintigraphy 4.0
- Refer to procedures guideline for more detail

## Slide 37
Normal pediatric bone scan increased radiotracer activity in the epiphysis (growth plates)
Growth Center
  Constochondral junction
  Most intense
  -proximal humorous
  -distal femur
  -proximal tibia
Costochondral junctions
Label the Scan – Ant/Post – L/R
https://radiopaedia.org/

## Slide 38: Whole Body Bone - continue
Always place camera as close as possible to the patient
Use whole body contouring if available
Acquire spots if needed
  Spot views
    256 x 256 Matrix
    Suggest - 500k to 1000k image at axial skeleton and then preset the time
Notes: TAKE TIME TO USE CAMERA LAB

## Slide 39: Limited Bone Scan
Usually several spot views
Similar to a three-phase bone, but without the first two phases
Study with limited views of skeleton
Spot views
  256 x 256 Matrix
  LEPH
  Suggest - 500k to 1000k image at axial
  skeleton and then preset the time
  Remember the body is bilaterally
  Symmetrical – always include the
  contra lateral side
https://radiologykey.com/identifying-bone-metastases/

## Slide 40
On a rare occasion a pinhole image is required
  Gives very high resolution images
  Assess greater detail
  May be used in infants, pediatric, and small structures
Acquisition parameters
  75 – 100k images
  Apply zoom if necessary
Limited Bone Scan - Pinhole
https://numebook.cl/artmes/NMDigitalBook/Skeletal/ANpertes.htm

## Slide 41: Single Photon Emission Tomography SPECT
May help to identify the presence of disease and location
Best applied where there is overlapping bone with questionable disease
  Ex. WBB identifies questionable uptake in a vertebral body
  SPECT is order better identify the presence and location of disease
Image contrast is improved
Spatial resolution is not, whoever depth information is revealed
Positioning is critical

## Slide 42: Normal SPECT Bone and Whole Body
Coronal
Transverse
Sagittal

## Slide 43: SPECT Continues
Acquisition Parameters
3600 rotation – elliptical or body contouring preferred
Two headed camera preferred
Spots 60 to 120
Matrix 64 x 64
10 to 40 seconds per stop
  The greater the time per stop the greater the count
Rule of thumb – Acquisition time should never be more than 30 minutes
  Concern for patient movement
SPECT Processing
See manufacturers/software guidelines for processing.
Integral and differential uniformity should be < 3.0
Center of Rotation (COR) should be done weekly
  Variation should be <0.5 pixel
Suggested filters
  Hanning and Butterworth to liminate high frequencies
  Ramp to eliminate low frequencies
  Pre/post image smoothing may be required

## Slide 44
Tail on Detector
Acromion Process
Views, Projections, and Artifacts
Lateral, Plantar, and Palmar

## Slide 45: Tail on Detector (TOD)

## Slide 46: Acromion Process
Tip of scapula overlying rib
https://pubs.rsna.org/doi/10.1148/rg.232025103
Hot spot is a cervical osteophyte

## Slide 47: Views/Projections/Angles and artifacts
Spot view reviews free pertechnetate
That accumulates in the stomach and
thyroid
Attenuation defect – Have the patient
Remove all jewelry
https://med.emory.edu/

## Slide 48: Views/Projections/Angles and artifacts
https://med.emory.edu/

## Slide 49: Lateral Skull

## Slide 50: Plantar/Lateral/Palmar
https://pubs.rsna.org/doi/10.1148/rg.232025103

## Slide 51: Part III
Technical Considerations
Contrast Enhancement
Collimation
Scan Speed
Matrix size
PHA and Windowing
Pitfalls in Tagging
Size
Age

## Slide 52: Contrast Enhancement
Setting the gray scale in normal contrast is 0 to 100%
Adjusting the scale 0 to 80% translates to pixels counts that are between 80% to 100% all equal 100%
  Does it hide the lesion on the top of the skull?
Adjust the gray scale 20 to 100% translates to all pixels between 0 to 20% have zero counts
  How does this effect rib uptake
Key – Adjusting contrast can have a negative consequence

## Slide 53: Contrast – Inverse
How do you display your images?
Black on White or white on black?
Adjusting the gray scale in this manner may improve image contrast

## Slide 54: Contrast – Removing the Hottest Pixel
Computer identifies the hottest pixel and in this case it is the urinary bladder - A
Adjusting the image contrast has NO effect
Draw an ROI around the bladder and remove and cut out the unwanted activity - B
Now image contrast can be adjusted to since the hottest counts occur in the bone

## Slide 55: Contrast – Color Scale
Gray scale set to 256 has 256 shades of gray
Adding color adds to image contrast
  Applying all color- Red, Green, Blue = 2653 shades of contrast
  Three examples of different color scales applied to a bone scan
What do you find acceptable?
Key – adding color(s) adds greater variability with contrast. Does this always improve image contrast?

## Slide 56: WB contouring
WB does improve image contrast and resolution.
The closer the detector is to the patient the less scatter is acquired
The greater amount of true counts are collected
If the body contouring mechanism fails. The adjustment of detector distance can be done manually

## Slide 57
Amount of scatter effected by:
  Patient size
    Larger patients have increased scatter
  Increased organ / detector distance
    Increase in gamma absorption by tissues
    Images degraded because gammas never reach detector
Factors Affecting Bone Images

## Slide 58: Collimation and Septa
Collimators are composed of lead septa and are usually designed to be parallel to each other
Gamma-rays that fall within the septa’s penumbra are collected and accepted as counts
Gamma-rays are outside the penumbra run into lead and are either absorbed or loose enough energy that the imaging system rejects the lower energy photon via the pulse height analyzer

## Slide 59: Applying Collimator Design
The goal of a collimator is to bring in as many true counts as possible
True counts accepted in the area of interest occur in the area of the Umbra
  Ideally only those counts coming from the umbra are counts coming from the correct location of the gamma event
Scatter counts originate inside the penumbra and are recorded
Important concept
  The closer the detector is to the patient the less scatter. This improves image contrast
  The further away the detector is from the patient the greater the scatter counts. This has a negative effect on image contrast/resolution

## Slide 60: Types of Parallel Whole Collimators
Length of the septa
General All Purpose (GAP) is a trade off between bringing in all count within the penumbra, therefore increasing count density
  At issue is that this larger penumbra brings in greater scatter counts negatively impacting image resolution
Most NMT departments have a High Resolution (HR) collimators
  Is the most common (LEHR) collimator utilized in an NMT department
  Significantly reduces scatter counts
Ultra High Resolution (UHR) further improves spatial and contrast resolution by eliminating more scatter counts

## Slide 61: WB Bone and Scan Speed
Suggested scan speed for WB bone ranges between 8 to 15 cm per minute (ACR)
The slower your scan speed
  The greater your count density and the better the resolution
  Negative – greater the possibility of patient motion
The faster the scan speed
  The lower your count density with a loss in resolution
  Positive – less probability for patient movement
Goal – Assess patient tolerance and go as slow as you can

## Slide 62: Matrix
An image is composed picture elements = Pixels
  In NM a pixels contain counts
  The greater the counts the greater the pixel density
  The more pixels and counts there are the better the spatial resolution
Matrix size, pixels, and imaging
  A 64 x 64 matrix contains 4096 pixels – less resolution
  256 x 256 matrix contains 65536 pixels – greater resolution
The following image is the relationship a between collimation and matrix size – as suggested by this author
  Variation may apply

## Slide 63: Examples of Different Matrix Sizes
https://radiologykey.com

## Slide 64: Pulse Height Analyzer and Windowing
PHA is usually set at 20% based on the energy of the incoming game
  140 keV x 0.2 = 28 kev ÷ 2 = ±14 keV
  Lower Lever Discriminator (LLD) = 126 keV
  Upper Lever Discriminator (ULD) - 154 keV
Only those photons that fall within the window are accepted
  Below the LLD are rejected
  Above the ULD are rejected

## Slide 65: Effects of PHA displacement
  The images on display are of a flood field uniformity test.
Uniformity of the system is lost if
  The 20% is center left of peak
  The 20% is center right of peak
Conclusion – Misplacement of the energy peak will cause image distortion
  Generating cold or hot artifacts

## Slide 66: Pitfall with Tagging MDP
Poor tag of the radiopharmaceutical can generate too much free 99mTc pertechnetate
This can be an issue with the manufacturer via a production problem or
Re-oxidation of 99mTc by injecting air into the MDP vial. O2 in the air causes the tag to breakdown
Free pertechnetate is notice by
  Stomach, thyroid, salivary uptake uptake
  Increase in soft-tissue
https://link.springer.com/chapter/10.1007/978-3-662-44169-5_4

## Slide 67: Pertechnetate Scan
Without an MDP on board this image shows you the distribution of free pertechnetate
  Salivary
  Stomach
  Thyroid
  Kidneys (not seen)
  Urinary bladder

## Slide 68: Factors Affecting Bone Images
Effects of increased body attenuation
  Example 1 – 85 kg male
  Example 2 – 125 kg male
Increase in body mass increases
  Attenuation of the gamma photon
  Increases the distance between detector and patient

## Slide 69: Patient age affects image
Infant to 21 years of age
  Growth plates
  Cartilage appears hotter
Twenty-one to ~60 years
  High quality bone scan unless the patient is overweight or has renal disease
Sixty-plus
  Reduced bone uptake due to decrease in bone density
  Focal areas of uptake do to arterial calcifications and/or arthritis

## Slide 70: Part IV
Diagnostic Potential Application of Non-Cancerous Bone Diseases

## Slide 71: Intra-arterial Injection
↑ increased concentration of activity in blood flow to those bones caused by arterial delivery of the radiotracer
  Referred to as the Glove Effect

## Slide 72: Dental – Infection vs Primary bone Ca
Image on the right is osteomyelitis that occurred post tooth extraction
Image on the right is osteosarcoma of the left maxilla
While there is a difference in uptake intensity, it would appear difficult to differentiate disease
This is a good example of why it is so important to take a complete patient history
https://pubmed.ncbi.nlm.nih.gov/12521065/
72

## Slide 73
Initial assessment of bone a bone graft can be misleading
One week post activity is usually intense, but appears to show viable bone tissue
  Excessive “trauma” to the bone makes it difficult to evaluate viability
One month post graft activity in the same area shows lack of bone uptake indicating failure.
Bone Graft
https://onlinelibrary.wiley.com/doi/abs/
10.1034/j.1399-0020.2000.290410.x

## Slide 74: Ascites
At times ascites may contain 99mTcMDP and can also be related to some type of carcinoma
This is an example of a patient that has peritoneal carcinomatosis from an unknown primary
CT shows significant fluid build-up which is also reflected in the WWB scan
https://www.sciencedirect.com/science/article/pii/S0001299814000671

## Slide 75: Medallion Effect
distal portion of manubrium photopenic - "medallion effect"
Sternoclavicular joints

## Slide 76
Recent or healing surgical wounds / fx may have ↑ increased uptake
Surgical Wound and Fracture

## Slide 77: Breast Uptake / Shadow
Breast activity or Shadow may appear in a bone scan
Increased uptake or breast shadow may be due to
  Lactation
  Calcification
  Mild soft-tissue uptake
Breast shadow may also be noted, however, an example is not given

## Slide 78: Incidental Findings
Three hours post injection of 99mTcMDP yielded the following image defining bilateral uptake of the pectoralis muscle
It appears that the patient had a extensive workout 48 hours prior to this bone scan
Extreme stress on muscle may cause trauma causing uptake of this radiotracer
https://journals.lww.com/nuclearmed/Fulltext/2004/12000/

## Slide 79: Renal Imaging in a Bone Scan
Sometimes this is a serendipitous finding – R/O renal disease
Example 1 – Renals appear to be excreting very little radio-urine
  Suggest a diuretic to see if there is a blockage, which was not done on this patient
Example 2 – Dilated ureters are identified and may be an indication of partial obstruction

## Slide 80: Processing – Inflammatory Sacroiliitis
Draw region 1 around the hottest area of the sacroiliac joint
Draw region 2 around then midpoint of the sacrum
Region 1 ÷ Region 2
  1.1 to 1.55 Normal
  1.55 to 1.75 Equivocal
  >1.75 inflammatory sacroiliitis

## Slide 81: Osteomyelitis
  Need to distinguish from cellulitis and osteomyelitis
    Cellulitis - short term antibiotics
    Osteomyelitis - long term (>6 months) expensive antibiotics

## Slide 82
  Three phase essential
  ↑ Increased blood flow on perfusion indicates inflammation
  Shows ↑ increased uptake on all three phases, while cellulitis is only first two phases
  May use Ga-67 or WBC for additional assessment in with infection
Osteomyelitis

## Slide 83: Osteomyelitis
Osteomyelitis involving the left proximal tibia
R
L
83

## Slide 84: Osteomyelitis vs Cellulitis
Three-Phase Bone scan to evaluate osteomyelitis
↑ Increased blood flow on perfusion indicates inflammation
Example 1 – Has increase in uptake in ALL three phases which indicates osteomyelitis
Example 2 – Increase in uptake occurs in the first two phases, but not on the delays indicating cellulitis
https://www.researchgate.net/publication/51526933

## Slide 85: Osteomyelitis
R
L
Here is another example of osteomyelitis

## Slide 86: Fractures / Trauma
Stress fx may take 7-10 days show depending on severity on an x-ray
    bone bruise, fx of carpal/tarsal bones, sternum, scapula, compression fx
Dx depends on location, extent, age of fx
Nuclear Studies typically show Fx/Trauma
  80% (+) from 24-72 hours
  95% (+) after 72 hours
Ninety percent of fx returns to normal in 2 hears
https://pubmed.ncbi.nlm.nih.gov/536788/

## Slide 87: Fractures / Trauma
Fracture – increased area of uptake at fracture
Two examples are displayed

## Slide 88: Fracture
Patient dropped a metal drawer on their left foot.
X-ray reveals NO fx
The pain in his foot persisted for three months
A bone scan was ordered
Images identify a fx in the left foot
Follow-up radiographs were still normal
http://gamma.wustl.edu/bs003te244.html

## Slide 89: Fractures / Trauma
Limb fractures at different stages of healing are also very suspicious because of the strong suspicion of intentional trauma (child abuse)
A comparison of a normal pediatric image and one of child abuse is noted and identified

## Slide 90: Fractures / Trauma –Shin Splints
Example 1 - “Shin splints” or medial tibial stress syndrome is caused by excessive muscle stimulation to the cortical bone, but is not a stress fracture
Example 2 0 If the pain and stress continue the lesion may extend 50% into the cortex bone defining a stress fracture
https://www.aspetar.com/journal/viewarticle.aspx?id=301#.YQAHFed7mUk

## Slide 91: Complex Regional Pain Syndrome (CRPS)
This painful disorder may result from different causes
  Fractures that damage nerve
  Surgery resulting in nerve damage
  Trauma to connective tissue
Reflex sympathetic dystrophy (RSD) is an older definition
This three phase bone scan confirms CRPS of the right hand and forearm
https://www.researchgate.net/publication/8076093

## Slide 92: Another example of CRPS
Images Courtesy of: J e r o l d W a l l i s , M . D .
w a l l i s @ n u c s 3 d . w u s t l . e d u

## Slide 93: Bone viability—loosening
Three-phase bone scan can be used to identify infection and/or loosening of this hip prosthesis
  99mTcMDP indicates increased uptake around the prosthesis that could e caused by either infection or loosening.
111In-WBC is then administered with 4 and 24 hour images are acquired
  The 4-hour image shows bilateral symmetry
  24-hour image identifies uptake at the distal end of the prosthesis ruling out loosening, however, infection appears to be the cause of the patients discomfort
https://www.researchgate.net/publication/234158094

## Slide 94
Example 1 - At first there is absence of tracer due to the loss of blood flow to the necrotic tissue
Example 2 - Increase of activity can also be seen around the of necrosis as the osteoblastic activity response to the fracture
  R-Hip 1 month post
  L-Hip 3 years post
AVN - Avascular Necrosis

## Slide 95: Frost Bite
Following cocaine use patient was exposed to -19oC
Arrived at the ED with swollen fingers where a 3-phase bone scan was completed
57Co markers were placed 2nd through 4th digits bilaterally
There appears to be significant loss of bone tissue

## Slide 96: Metabolic disease
Hyperparathyroidism
Parathyroid adenoma generates excessive levels of parathyroid hormone
  Increases bone turnover
  Resulting in an increase 99mTcMDP uptake
https://www.mja.com.au/journal/2010/193/7

## Slide 97: Metabolic Disease
Hypertrophic Pulmonary Osteoarthropathy
Certain lung cancer generate parathyroid hormone
  Generating excessive bone turnover, much like hyperparathyroidism

## Slide 98: Metabolic Disorders
Osteomalacia
Usually effects the entire bone structure
  Often related to Vitamin D or calcium deficiency
  Causes bone softening via defective mineralization
99mTcMDP uptake is increased throughout the skeletal system
https://tech.snmjournals.org/content/41/4/299

## Slide 99: Metabolic Disease
Paget’s Disease
Benign disease of unknown etiology
Paget’s is an a combination of abnormal bone destruction and regrowth.
Abnormal bone formation can be found in the pelvis, segments of long bone, and the skull.
http://www.e-radiography.net/radpath/p/pagets.htm
No longer an active link

## Slide 100: Joint Imaging
Arthritis
  Used to evaluate inflammations involving bones, joints
  Need bone and blood flow/pool
  Use pinhole collimator for high resolution

## Slide 101: Joint Scan – Osteo/Rheumatoid arthritis
Example 1 – Osteoarthritis
  Shows no uptake in the first two phases of a three phase bone scan
  Delayed images identify activity within the involved joint space
Example 2 – Rheumatoid arthritis
  Shows increased uptake in all phases of a three phase bone scan
  This appears to be related to synovial involvement of the disease

## Slide 102: Bone Trauma vs. Metastatic Disease
Bone trauma tends to have a very specific pattern as seen in the first example
Metastatic disease tends to be very random as noted in the second example

## Slide 103: Diagnostic Potential Application of Cancerous Bone Diseases

## Slide 104: Part V
Diagnostic Potential Application of Cancerous Bone Diseases

## Slide 105: Primary Tumors
Ewing's sarcoma
  Cell origin Primitive Neuroectodermal Cell
The child underwent 3-months of treatment. Exact type was not identified.
108

## Slide 106: Primary Bone Tumors
Usually solitary – knees, long bones, skull
Primary bone cancer is more prevalent in pediatrics
Rarely metastasizes to distant sites (possibly lung) but can metastasize to bone
Scan for vascularity and to determine number or localization of sites

## Slide 107: Osteoid Osteoma
Benign bone-forming tumor
  Sometime referred to as “double uptake” or “double density”
  May cause swelling and inflammation
  Treated with anti-inflammatory drugs or surgery

## Slide 108: Malignant Pleural Effusion
Kosuda S and colleagues evaluated pleural effusion and determined that 99mTcMDP uptake maybe associated ~50% as malignant.
Usually unilateral
It occurs by passive trasudation
https://med.emory.edu/
https://pubmed.ncbi.nlm.nih.gov/2223379/

## Slide 109: Osteosarcoma
Most common malignant bone tumor in children
Cell origin osteoblast
Treat chemotherapy and surgery
Sclerotic destruction: “sunburst”

## Slide 110: Ewing Sarcoma
Second most common malignant bone tumor in children
Cell origin Primitive Neuroectodermal Cell
Treat chemotherapy, surgery and radiation therapy
Lytic with laminar periosteal elevation
Statistically found
  45% lower limb
  25% pelvis
  13% upper limb
  13% Sine/rib
http://radiopaedia.org/cases/ewing-sarcoma-pelvis

## Slide 111: Primary Tumors
Metastases (Mets)
  80% with known neoplasms and bone pain have mets on scan
  30-50% of patients with mets have no pain
  Bone scan is 95% sensitive in detecting mets

## Slide 112
  Lesions can be detected 6 months earlier than x-ray
  Usually have ↑ increased uptake of RP*
  Multiple focal lesions throughout skeleton (axial 60%)
  Baseline and follow-up
Metastatic Bone Disease

## Slide 113
Metastatic Bone Disease

## Slide 114: Osteosarcoma with Soft Tissue Uptake
Cell origin osteoblast
114

## Slide 115: Super Scan
≥ 50% of RP localizes in bone
Faint to absent kidneys
Reduced or no activity in the urinary bladder
Decreased body background
This is an example of excessive metastatic diseases
Similar distribution can be see with patients that have hyperparathyroidism
https://www.semanticscholar.org/paper/Musculoskeletal-case-27.-Diagnosis/

## Slide 116: Irradiated Bone and the Flare Phenomenon
  Response to Radiation Therapy
    Photopenic pattern may occur – 60% with a mean dose of 3750 rad
    Flare phenomenon can also be generated
  Flare phenomemon can occur with chemo, radiation, and/or hormonal therapy
    Increased uptake reflects repair and healing
  Bone returns to normal in 3 to 6 months but may take up to 2 years

## Slide 117: Additional Required Reading
https://www.acr.org/-/media/ACR/Files/Practice-Parameters/Skeletal-Scint.pdf