Xilinx ISE 9.2 schematic based simulation

Open the T1.ise project created in the Digilent S3 schematic ISE 9.2 tutorial. Select and double right click on xc3s200-4ft256. Verify that the ISE Simulator is selected, and close the window.

Select Project ( New Source.

Enter TB_T1 for the test bench file name and select “Test Bench Waveform”.

Click on Next, and in the next window be sure T1top is selected.

Click on next and then finish.

Select Combinatorial under Clock Information, and click ion Finish.

A timing waveform will now appear this shows the SW (switch) input signals and the LD (LED) output signals. By clicking in the blue area you can set to SW signals High or Low to generate a stimulus waveform.

Select Behavioral Simulation. Then double click on Simulate Behavioral Model under Xilinx ISE Simulator.

I had to do this twice. I think the first time the test bench had not been added to the project. The second run produced the waveform shown below appeared.