Numeric_std conversions

library IEEE;     use IEEE.std_logic_1164.all;

use IEEE.numeric_std.ALL;

ENTITY tb IS END tb;

ARCHITECTURE test OF tb IS

signal x, y: unsigned(2 downto 0) := (others => '0');

signal a, b: signed(2 downto 0) := (others => '0');

signal m, n, o: integer range -15 to 15;

BEGIN

n <= n + 1 after 5 ns;

x <= TO_UNSIGNED(n, 3);     	-- Integer n to 3 bit unsigned

a <= TO_SIGNED(n, 3);  		-- Integer n to 3 bit unsigned

y <= UNSIGNED(a);			-- Signed to Unsigned

b <= SIGNED(y);			-- Unsigned to Signed

m <= TO_INTEGER(x);		-- Unsigned to integer

o <= TO_INTEGER(a);		-- Signed to integer

END TEST;

IEEE.STD_ARITH.ALL

library IEEE;

use IEEE.STD_LOGIC_1164.ALL;

use IEEE.STD_LOGIC_ARITH.ALL;

use IEEE.STD_LOGIC_UNSIGNED.ALL;

ENTITY tb IS END tb;

ARCHITECTURE test OF tb IS

signal slv_1, slv_2: std_logic_vector(2 downto 0) := (others => '0');

signal u_1, u_2: unsigned(2 downto 0) := (others => '0');

signal s_1, s_2: signed(2 downto 0) := (others => '0');

signal n, i_1, i_2, i_3: integer range -15 to 15;

BEGIN

n <= n + 1 after 5 ns;

slv_1 <= CONV_STD_LOGIC_VECTOR(n, 3);

u_1   <= CONV_UNSIGNED(n, 3);

s_1   <= CONV_SIGNED(n, 3);

slv_2 <= CONV_STD_LOGIC_VECTOR(u_1, 3);

sl_2 <= CONV_SIGNED(u_1, 3);

u2_2  <= CONV_UNSIGNED(s_1, 3);

i_1 <= CONV_INTEGER(slv_1);

i_2 <= CONV_INTEGER(u_1);

i_3 <= CONV_INTEGER(s_1);

END TEST;