KIPS register transfer operations Version 3.4

ALU related combinational logic

| SA := A | ALU := SA + SB |
| --- | --- |
| SA := PC | ALU := SA - SB |
| SA := | ALU := SA & SB |
| SB := B | ALU := SA ¦ SB |
| SB := 4 | ALU := 0 |
| SB := (n | ALU := 1 |
| SB := (ofst¦¦00 | ALU := SA |
| SB := | ALU := SB |

Register transfer operations Version 3.4

| PC ( PC | IR ( IR | RS ( RS |
| --- | --- | --- |
| PC ( 0 | IR ( M(PC)( | RT ( RT |
| PC ( PC + 4 |  | RD ( RD |
| PC ( ALU | ALUout ( ALUout | RT ( MDR |
| PC ( ALUout | ALUout ( ALU | RD ( MDR |
| PC ( PC(31..28)¦¦addr¦¦00 |  | RT ( ALUout |
| MDR ( MDR | M(ALUout) ( B( | RD ( ALUout |
| MDR ( M(ALUout)( |  | B ( B |
| MDR ( ALU( | A ( A | B ( RT |
| MDR ( ALUout( | A ( RS | B ( MDR |
| MDR ( M(PC)( | A ( MDR( | $31 ( MDR |
|  |  | $31 ( ALUout |

The above defines are the lowest level register transfer operations. To describe the operations of the control unit using a state diagram, we will specify register operations at a slightly higher level. For example if no specification is entered for a certain register it is understood that the register retains its value. i.e. We will not enter IR ( IR this is understood. As another example, suppose we want to put the contents of the B register into the MBR register, we will write MDR ( B, instead of writing MDR ( ALU, ALU := SB, and SB := B. There may be certain operations that cannot be performed during the same clock cycle

The KIPS Instruction Set (with new instructions)

| lw | rt,ofst(rs) |  | rt ( M(rs + (ofst) |
| --- | --- | --- | --- |
| 100011 | rs | rt | Ofst |
| sw | rt,ofst(rs) |  | M(rs + (ofst) ( rt |
| 101011 | rs | rt | Ofst |
| beq | rs,rt,ofst |  | if rs=rt then PC(PC +(ofst¦¦00 else PC ( PC+4 |
| 000100 | rs | rt | Ofst |
| add | rd,rs,rt |  | rd ( rs + rt |
| 000000 | rs | rt | rd | 00000 | 000000 |
| sub | rd,rs,rt |  | rd ( rs – rt |
| 000000 | rs | rt | rd | 00000 | 010010 |
| and | rd,rs,rt |  | rd ( rs & rt |
| 000000 | rs | rt | rd | 00000 | 000100 |
| or | rd,rs,rt |  | rd ( rs ¦ rt |
| 000000 | rs | rt | rd | 00000 | 010101 |
| slt | rd,rs,rt |  | If rs < rt then rd (1 else rd (0 |
| 000000 | rs | rt | rd | 00000 | 011010 |
| j | addr |  | PC ( PC(31..28)¦¦addr¦¦00 |
| 100000 | Addr |
| addi | rd, rs, n |  | rd ( rs + (n |
| 100000 | rs | rt | Ofst |
| jal | addr |  | $31 ( PC + 4, PC ( PC(31..28)¦¦addr¦¦00 |
| 000011 | Addr |
| jr | rs |  | PC ( rs |
| 000000 | rs | 00000 | 00000 | 00000 | 100000 |
| wai | rt |  | rt (PC |
|  |  | rt |  |
| lwr | rd, rs, n |  | Rd ( M(Rs + Rt) |
|  | rs | rt | Ofst |
| swx | rt,ofst(rs) |  | M(rs) ( rt, rs ( rs+ (ofst |
|  | rs | rt | 00000 | 00000 | 100000 |

SWX: ALUout ( A(Rs); M(ALUout(Rs)) ( B(RT), MDR ( A+(ofst;  Note: Rs ( MDR (requires adding rs input to write reg mux)

The control unit FSM described using a pseudo HDL. Showing implementation of J. BEQ, R-Type, LW and SW.

IF Reset then Goto S0

S0: 	PC ( PC + 4, IR ( M(PC), goto S1

S1:	A ( Rs, B ( Rt,

ALUout ( PC + (n||00	i.e. ALUout ( ALU := (SA := PC) + (SB := 4)

if op = J goto S9, if op = BEQ goto S8, if op = R-type goto S6

if op = LW or SW goto S2

S2:	ALUout ( A + (ofst

i.e.  ALUout ( ALU := (SA := A) + (SB := (ofst)

if op = LW goto S3

if op = SW goto S5

S3:	MDR ( M(ALUout), goto S4

S4:	Rt (MDR, goto S0

S5:	M(ALUout) ( B, goto S0

S6:	ALUout ( A * B	i.e. ALUout ( ALU := (SA := A) * (SB := B)

goto S7

S7:	Rd ( ALUout, goto S0

S8:	if A = B then PC ( ALUout

Goto S0

S9:	PC ( PC(31..28)||addr||00

goto S0

The control unit FSM described using a pseudo HDL. Showing implementation of J. BEQ, R-Type, LW and SW.

Non-deterministic version.

IF Reset then Goto S0

S0: 	PC ( PC + 4, IR ( M(PC), goto S1

S1:	A ( Rs, B ( Rt,

ALUout ( PC + (n||00	i.e. ALUout ( ALU := (SA := PC) + (SB := 4)

if op = J goto S9, if op = BEQ goto S8, if op = R-type goto S6

if op = LW or SW goto S2

S2:	ALUout ( A + (ofst

i.e.  ALUout ( ALU := (SA := A) + (SB := (ofst)

if op = LW goto S3

if op = SW goto S5

S3:	MDR ( M(ALUout), goto S4 and S0

S4:	Rt (MDR, goto Null

S5:	M(ALUout) ( B, goto S0

S6:	ALUout ( A * B	i.e. ALUout ( ALU := (SA := A) * (SB := B)

goto S7 and S0

S7:	Rd ( ALUout, goto Null

S8:	if A = B then PC ( ALUout

Goto S0

S9:	PC ( PC(31..28)||addr||00

goto S0

The control unit FSM described using a pseudo HDL. Showing implementation of J. JR, BEQ, R-Type, Immediate type, LW and SW.

IF Reset then Goto S0

S0: 	PC ( PC + 4, IR ( M(PC), goto S1

S1:	A ( Rs, B ( Rt,

ALUout ( PC + (n||00	i.e. ALUout ( ALU := (SA := PC) + (SB := 4)

if op = J goto S9, if op = BEQ goto S8, if op = R-type goto S6

if op = LW or SW goto S2

if op = Imm goto S10

if op = JR goto S11

S2:	ALUout ( A + (ofst||00

i.e.  ALUout ( ALU := (SA := A) + (SB := (ofst||00)

if op = LW goto S3

if op = SW goto S5

S3:	MDR ( M(ALUout), goto S4

S4:	Rt (MDR, goto S0

S5:	M(ALUout) ( B, goto S0

S6:	ALUout ( A * B	i.e. ALUout ( ALU := (SA := A) * (SB := B)

goto S7

S7:	Rd ( ALUout, goto S0

S8:	if A = B then PC ( ALUout

Goto S0

S9:	PC ( PC(31..28)||addr||00

goto S0

S10:	ALUout ( A * (n		i.e. ALUout ( ALU := (SA := A) * (SB := (n)

goto S12

S11:	PC ( A, goto S0

S12: Rt( ALUout, goto S0

# Footnotes

Assume I have added the new capability to reset the PC.

Assume I have added the new capability to increment the PC by 4 without using the ALU.

( This is a Memory write it cannot be done at the same time as a memory read.

( This is a Memory read it cannot be done at the same time as a memory write.

( Assume I have added this new capability to the design in the book

rs and rt are treated as signed integers.

# Text boxes

S2

ALUout ( A+(offset