HW 02

Due 9/8/09

- Consider case when n = 16. Show how to compute in the least time using a four-segment pipeline.

| Seg |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Time | Input | S1 | S2 | S3 | S4 | Output |
| 0 | A1,A2 | A1+A2 |  |  |  |  |
| 1 | A3,A4 | A3+A4 | A1+A2 |  |  |  |
| 2 | A5,A6 | A5+A6 | A3+A4 | A1+A2 |  |  |
| 3 | A7,A8 | A7+A8 | A5+A6 | A3+A4 | A1+A2 |  |
| 4 | A9,A10 | A9+A10 | A7+A8 | A5+A6 | A3+A4 | A1+A2 = P1 |
| 5 | A11,A12 | A11+A12 | A9+A10 | A7+A8 | A5+A6 | A3+A4 = P2 |
| 6 | A13,A14 | A13+A14 | A11+A12 | A9+A10 | A7+A8 | A5+A6 = P3 |
| 7 | A15,A16 | A15+A16 | A13+A14 | A11+A12 | A9+A10 | A7+A8 = P4 |
| 8 | P1,P2 | P1+P2 | A15+A16 | A13+A14 | A11+A12 | A9+A10 = P5 |
| 9 | P3,P4 | P3+P4 | P1+P2 | A15+A16 | A13+A14 | A11+A12 = P6 |
| 10 | P5,P6 | P5+P6 | P3+P4 | P1+P2 | A15+A16 | A13+A14 = P7 |
| 11 | P7,P8 | P7+P8 | P5+P6 | P3+P4 | P1+P2 | A15+A16 = P8 |
| 12 |  |  | P7+P8 | P5+P6 | P3+P4 | P1+P2 = Q1 |
| 13 | Q1,Q2 | Q1+Q2 |  | P7+P8 | P5+P6 | P3+P4 = Q2 |
| 14 |  |  | Q1+Q2 |  | P7+P8 | P5+P6 = Q3 |
| 15 | Q3,Q4 | Q3+Q4 |  | Q1+Q2 |  | P7+P8 = Q4 |
| 16 |  |  | Q3+Q4 |  | Q1+Q2 |  |
| 17 |  |  |  | Q3+Q4 |  | Q1+Q2 = R1 |
| 18 |  |  |  |  | Q3+Q4 |  |
| 19 | R1,R2 | R1+R2 |  |  |  | Q3+Q4 = R2 |
| 20 |  |  | R1+R2 |  |  |  |
| 21 |  |  |  | R1+R2 |  |  |
| 22 |  |  |  |  | R1+R2 |  |
| 23 |  |  |  |  |  | F = R1+R2 |
| 24 |  |  |  |  |  |  |
| 25 |  |  |  |  |  |  |
| 26 |  |  |  |  |  |  |
| 27 |  |  |  |  |  |  |

T(16) = 23

For the next two problems, show your work and answer each problem for N = 5 and N = 8.

- Using a four segment pipeline with the restriction that the pipeline must empty before a new type of operation begins, show how to compute  in the fastest possible time.

- Repeat 2 without the restriction that all segments must do the same operation.

Solutions to #2:

T4(5) = 20

T4(8) = 26

Repeating the above for various values of n, I obtained,

Solutions to #3:

T4(5) = 17 segment times

T4(8) = 23 segment times.

The general solution for 2 is the upper bounds for 3, since 2 will never be faster than 3. The best problem 3 times I obtained for various values of n are:

For problems 4 through 6 write a single Mips instructions to perform the following operations.

- Set all bits of $a0 to ‘0’.

Solutions include:

addi $a0, $0, 0

add  $a0,$0,$0

and $a0,$0,$0

addi $a0,$0,0

etc.

- Set all bits of $a0 “1'.

Solutions include:

addi $a0,$0,-1

nor $a0,$0,$0

- Set the most significant bit of $a0 to ‘1’ and set all other bits of $a0 to ‘0’;

Solutions include:

lui  $a0, 0x8000

lui	 $a0,0x8000

- Set the least significant bit of $a0 to ‘1’ and set all other bits of $a0 to ‘0’.

Solutions include:

slti	$a0,$0,1

addi $a0,$0,1

ori $a0,$0,1

- Fill in below the two instructions required to complete the MIPS program to compute the sum .

main:

and     $s0,$0,$0       #Set sum to 0

addi    $t0,$0,100      #Put count in $t0

loop:   add     $s0,$s0,$t0     #Increase sum by count

addi    $t0,$t0,-1      #Decrement count

bne     $t0,$0,loop     #Loop till count = 0.

DONE:   jr      $32             #Return with sum in $s0

# Footnotes

Enter pipeline at beginning of  T=0.