HW 02

Due 9/8/09

- Consider case when n = 16. Show how to compute in the least time using a four-segment pipeline.

| Seg |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Time | Input | S1 | S2 | S3 | S4 | Output |
| 0 | A1,A2 | A1+A2 |  |  |  |  |
| 1 |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |
| 9 |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |
| 11 |  |  |  |  |  |  |
| 12 |  |  |  |  |  |  |
| 13 |  |  |  |  |  |  |
| 14 |  |  |  |  |  |  |
| 15 |  |  |  |  |  |  |
| 16 |  |  |  |  |  |  |
| 17 |  |  |  |  |  |  |
| 18 |  |  |  |  |  |  |
| 19 |  |  |  |  |  |  |
| 20 |  |  |  |  |  |  |
| 21 |  |  |  |  |  |  |
| 22 |  |  |  |  |  |  |
| 23 |  |  |  |  |  |  |
| 24 |  |  |  |  |  |  |
| 25 |  |  |  |  |  |  |
| 26 |  |  |  |  |  |  |
| 27 |  |  |  |  |  |  |

T(16) = 23

For the next two problems, show your work and answer each problem for N = 5 and N = 8.

- Using a four segment pipeline with the restriction that the pipeline must empty before a new type of operation begins, show how to compute  in the fastest possible time.

- Repeat 2 without the restriction that all segments must do the same operation.

Mips problems:

For problems 4 through 7 write a single Mips instructions to perform the following operations.

- Set all bits of $a0 to ‘0’.

- Set all bits of $a0 “1'.

- Set the most significant bit of $a0 to ‘1’ and set all other bits of $a0 to ‘0’;

lui	 $a0,0x8000

- Set the least significant bit of $a0 to ‘1’ and set all other bits of $a0 to ‘0’.

- Fill in below the two instructions required to complete the MIPS program to compute the sum .

main:

and     $s0,$0,$0       #Set sum to 0

addi    $t0,$0,100      #Put count in $t0

loop:   ________________________#Increase sum by count

________________________#Decrement count

bne     $t0,$0,loop     #Loop till count = 0.

DONE:   jr      $32             #Return with sum in $s0

# Footnotes

Enter pipeline at beginning of  T=0.