EGRE 426

Homework

Due

Monday 9/29/09

Solutions

. Using a combination of CSA and CLA show the fastest way to add 16 partial products. You do not have to be concerned with minimizing the size of the adders, and you should assume that the propagation delay of the CLA is significantly longer that the CSA.

| P1 | P2 | P3 | P4 | P5 | P6 | P7 | P8 | P9 | P10 | P11 | P12 | P13 | P14 | P15 | P16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | CSA |  |  | CSA |  |  | CSA |  |  | CSA |  |  | CSA |  |  |
|  |  | CSA |  | CSA |  |  | CSA |  |  |  |  |
|  |  |  |  | CSA |  |  |  | CSA |  |  |  |  |  |  |  |
|  |  |  |  |  | CSA |  |  |  | CSA |  |  |  |  |  |
|  |  |  |  |  |  |  | CSA |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  | CSA |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  | CLA |  |  |  |  |  |

Worst case 6 CSA delays and 1 CLA delay.

Answer:

add	$t2,$t3,$0	# Move $t3 to $t2

bgtz	$t2,OK		# If positive done

sub	$t2,$0,$t2	# If negative make positive

OK:	…

Solution: Recall that

| lw | rt,ofst(rs) | rt ( M(rs + (ofst) |
| --- | --- | --- |

If A_lower(15) = 0 then A_upper_adjusted = A_upper. If A_lower(15) = 1 then A_upper_adjusted = A_upper + 1 then

$t0 = A_upper_adjusted|0000_0000_0000_0000 = A_upper|0000_0000_0000_0001

A_lower($t0) = $t0 + 1111_1111_1111_1111|A_lower =

= (A_upper + 1)|0000_0000_0000_0000 + 1111_1111_1111_1111|A_lower

= [A_upper + (1111_1111_1111_1111 + 1)] |A_lower  = A_upper|A_lower

Solution: Refer to the Four Bit Two’s Complement Addition Table in the Chapter 3 slides and observe that when the two numbers added and the result is treated as unsigned integers carry out occurs iff abd only ig $t3 + $t4 < $t3 and $t4. The sltu instruction compares registers treating the registers as unsigned integers. (See footnote 8 of MIPS instruction set handout). Therefore, the solution is:

addu	$t2,$t3,$t4

sltu	$t2,$t2,$t4 	or 	sltu	$t2,$t2,$t3

Solution:

- –1,391,460,350

- 2,903,506,946

- –8.18545 x 10-12

- sw $r16, $r8(16)

3.37 Show the IEEE 745 binary representation for the floating-point number 2010 in single precision.

Solution: 2010 = 101002 = 1.0100 x 24

Sign = 0, Significan = .010…, Exponent = 127 + 4 = 13110 = 10000011

0_10000011_01000000000000000000000