Chapter 5 homework

Due 10/6/09

- Refer to page 4 of the class handout and indicate in each if the operations can be done simultaneously. If they can be done on the same clock, identify the nature of the conflict.

a). MDR ( B, PC ( PC + (ofst||00

b).MDR ( A, PC ( PC + (ofst||00

c).MDR ( A, A ( MDR

d). MDR ( A, A ( MDR, IR ( M(PC), PC ( PC+4, B ( RT, ALUout ( A,

RT ( ALUout.

2.  Fill in the table below.

| Operation | Memory addr Mux | Memory Read Write | write register Mux | Write Data Mux | SA Mux | SB Mux | ALU control operation | PC Mux |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ALUout ( PC + (ofst¦¦00 | x | n | x | x | 0 | 3 | + | x |  |
| PC ( PC(31..28)¦¦addr¦¦00 | x | n | x | x | x | x | x | 2 |  |
| PC ( ALUout | x | n | x | x | x | x | x | 1 |  |
| PC ( PC + 4 |  |  |  |  |  |  |  |  |  |
| IR ( M(PC) |  |  |  |  |  |  |  |  |  |
| ALUout ( A + (ofst¦¦00 |  |  |  |  |  |  |  |  |  |
| ALUout ( A + (n |  |  |  |  |  |  |  |  |  |
| MDR ( M(ALUout) |  |  |  |  |  |  |  |  |  |
| RT ( MDR |  |  |  |  |  |  |  |  |  |
| RD ( ALUout |  |  |  |  |  |  |  |  |  |
| M(ALUout) ( B |  |  |  |  |  |  |  |  |  |
| ALUout ( PC |  |  |  |  |  |  |  |  |  |
| ALUout ( A - B |  |  |  |  |  |  |  |  |  |

x – don’t care. R, W, n – Memory read, write, neither read nor write.